## Slide 1
Midas Part II
Midas Deployment.
Known Midas implementations.
Utilities and usage.
Features & Hidden Features.
DEMO – part II

## Slide 2
Midas Deployment.
Europe | Canada
Bari - INFN, italy Fribourg University, Switzerland Kascade-Grande, Karlsruhe Trieste - INFN, Italy Uppsala University, Uppsala, Finland … | Carlton University, Ottawa Montreal University, Quebec, Canada Northern British Columbia University, BC, Canada Regina University, Regina, Saskatchewan, Canada Queen's University / NRCC, Ottawa, ON, Canada Victoria University, Victoria, BC, Canada Fuel Cell Technologies, Ontario, Canada …
USA | Other
Argonne National Lab, Chicago Brookhaven National Lab, NY Boulder, Colorado University Colorado School of Mines, Colorado CalTech, California Kentucky University LANL Los Alamos Michigan University Notre-Dame University, Indiana Virginia Tech, Virginia, VA … | JINR, Dubna Russia Peking University, China …
Notes: Each laboratory has at some point been in contact with us for question about installation, drivers, operations.

## Slide 3
  Suzannah Daviel DAQ, Triumf µSr, nmr.
  Peter Green DAQ, Uni. of Alberta NOVA analyzer.
  Greg Hackman Triumf 8, J73a SCSI driver.
  Gertjan Hofman Triumf CHAOS, stripchart.tcl.
  Paul Knowles Uni. of Fribourg rpm packaging, documentation.
  Rudi Meier Uni. of Tuebingen CHAOS, monitoring.
  Glenn Moloney Uni. of Melbourne CHAOS, Linux Camac drivers.
  Dave Morris Triumf SlowControl, Java.
  Konstantin Olchanski DAQ, Triumf Twist, SlowControl, ROOT.
  Renee Poutissou DAQ, Triumf Twist, web interface, mevb, lazylogger.
  Andreas Suter PSI Hvedit Qt interface.
  Piotr Adam Zolnierczuk Uni. of Kentucky rpm packaging.
Midas Contributors.
The Midas software package wouldn’t have been that good without the contribution of the following people and … potential users like you!
Notes: People who made some significant contribution to Midas from implementation suggestions to code writing.

## Slide 4
Use | Location | #Nodes | #FE | #EQ | #Poll | #SC | #Client | Data Rate | Hardware | OS | Comments
TWIST | TRIUMF | 4 | R3 | 12 | 2 | 8 | 15 | 6MB/s | VME/FB/CAMAC, Network/GPIB | VxWorks, Linux | Dual Logger, LazyLogger mevb, multiple nodes.
CHAOS (retired) | TRIUMF | 4 | R3 | 8 | 1 | 1 | 11 | 4MB/s | FB/CAMAC/VME | VxWorks, Linux,W2K | Dual logger, Lazylogger.
LTNO | TRIUMF | 2 | R1 | 18 | 1 | 11 | 9 | < 50KB/s | CAMAC(DSP004), Network,GPIB, RS232 | W2K,Linux | Hardware Histograms Readout, Software Histograms Readout, Large #SC, Qt run control.
Dragon | TRIUMF | 2 | R1 | 5 | 1 | 0 | 8 | < 50KB/s | CAMAC(HYTEC) | Linux | Buffered events, PAW, Lazylogger.
TUDA | TRIUMF | 3 | R1 | 2 | 1 | 0 | 4 | < 100KB/s | VME/ CAMAC(CBD8210) | VxWorks, Linux/Solaris | MIDAS-UK Solaris.
TRINAT | TRIUMF | 2 | R1 | 4 | 1 | 0 | 4 | < 100KB/s | VME/ CAMAC(CBD8210) | VxWorks, Linux | User code for PM gain control in FE, NOVA.
BetaNMR | TRIUMF | 3 | R1 | 9 | 1 | 2 | 6 | < 50KB/s | VME(MVME162), SIS3801 | VxWorks, Linux | Software Histogram Readout, Epics, Cycle Ctl within FE.
Polarimeter | TRIUMF | 1 | R1 | 3 | 1 | 0 | 2 | < 50Kb/s | VME(MVME162) | VxWorks, Linux | SC(Epics).
μSRs (3) | TRIUMF | 2 | R1 | 5 | 1 | 0 | 3 | < 50KB/s | VME/ CAMAC(CBD8210) | VxWorks, Linux | Software Histogram Readout, Large Event, Manual trigger.
Multi | TRIUMF | 2 | R1 | 3 | 1 | 0 | 5 | 2MB/s | VME/FastBus | VxWorks, Linux | FB data, filter in FE.
8Pi | TRIUMF | 2 | R1 | 2 | 1 | 0 | 3 | 100KB/s | VME(MVME162), CAMAC(CBD8210), SIS3801 | VxWorks, Linux | FERA/VME, CAMAC
Known Midas implementations I.
Notes: Over 15 Midas station are installed at Triumf. From simple scintillator test to full experiment.

## Slide 5
Known Midas implementations II.
Use | Location | #Nodes | #FE | #EQ | #Poll | #SC | #Client | Data Rate | Hardware | OS | Comments
GPS (2) | TRIUMF | 1 | 1 | 3 | 2 | 0 | 4 | 50KB/s | CAMAC(KCS2927) | Linux | Deferred Transition, Tiny events NOVA, 2Polls eqp.
Kopio (2) | TRIUMF | 1 | 1 | 2 | 1 | 0 | 3 | < 100KB/s | CAMAC(HYTEC) | Linux | PAW.
Dragon I | TRIUMF | 1 | 1 | 2 | 1 | 0 | 3 | < 100KB/s | CAMAC(HYTEC) | Linux | PAW.
Tigress I | TRIUMF | 2 | R1 | 2 | 1 | 0 | 4 | < 100KB/s | CAMAC(HYTEC) | VxWorks, Linux | Java control (JACQ).
DANCE (planned) | LANL | 15 | 14 |  |  |  |  | 1MB/s | 500MHz cPCI Kinetics 2913 (CAMAC) | Linux | mevb, ROOT.
MULAN | PSI | 12 | 10 |  |  |  | 20 | 5-10MB/s | PCI/ CAMAC(HYTEC) | Linux | mevb, ROOT.
Teaching | Uni. of Northern BC | 1 | 1 | 2 | 1 | 0 | 3 | < 50KB/s | CAMAC(SCSI) | Linux | PAW, simple.
Carleton | Ottawa | 1 | 1 | 2 | 1 | 0 | 3 | < 50KB/s | VME(SIS3100) | Linux | Multiple Flash ADCs, Hardware Histogram Readout, PAW.
PIBETA | PSI | 4 | 2 | 6 | 1 | 4 | 5 | < 100KB/s | VME(SBS617) FB(STR340) CAMAC(HYTEC) | W2K, Linux | PAW, Dual Lazylogger(FTP+Tape)
LEM | PSI | 3 | 1 | 6 | 2 | 4 | 8 | 3kb/s | CAMAC(HYTEC) | NT4,Linux | PAW
Det. Group | PSI | 1 | 1 | 2 | 1 | 0 | 1 | 1MB/s | CAMAC(HYTEC) | WXP | Fal, PAW
MEG (planned) | PSI | 20 | 5 | 7 | 1 | 5 | 10 | 120MB/s | VME(SIS3100) | Linux | mevb, ROOT
Notes: Reported here are few of the known experiments using Midas.

## Slide 6
Midas @ TRIUMF I - ISAC I
TUDA
DRAGON
BNMR
HV platform
(-60KV to +29KV)
Poster RT01
GPS/E823
OSAKA
LTNO
Talk RT03
Polarimeter
8Pi
GP2
Notes: TUDA: Silena ADC LTNO: DSPEC, AD413a Dragon: FERA, TDC3377 8Pi: SIS3700, SIS3801, AD413a
BNMR:SIS3801, PPG, FSC OSAKA: std CAMAC+GPIB Polarimeter: SIS3801 E823: AD413a, IS 10A, LRS3521, MM8206

## Slide 7
Midas @ TRIUMF II - TWIST
56 chambers (~4000 channels).
4 gas systems.
“high data rate” 2KEvts/s, 10MB/s.
Multiple FB crate -> Event Builder.
Large number of Slow control (TCP/IP, CAMAC, RS232, USB)
  Gas flow monitoring (~65 flows).
  Differential/Absolute pressure monitoring (10P)
  Temperature monitoring (~150T)
  Low V/I monitoring (300).
  Detector position monitoring (4 readout laser)
  Beamline magnet monitoring (B, T)
  Solenoid monitoring (B, T, strain gauge)
  Electronic racks (T,V)
  HV supplies (56V, 56I)
See RT03 – Poster
The TWIST Data Acquisition System at TRIUMF

## Slide 8
Twist
Notes: “Large” experiment are the main drive for software development and improvement. Initial experiment such as CHAOS at Triumf & PiBeta at PSI have been the main customers for Midas. A more recent experiment TWIST at Triumf has taken over that job and gave to Midas a chance to polish a lot of details as well as extending its capabilities.

## Slide 9
Midas Utilities
odbedit Online DataBase Editor.
dio Program launcher for Direct IO access.
mstat Status display.
mdump Event display utility.
mlogger Multi channel Data logger and history data collector.
mhist History data utility.
mchart ODB data for stripchart utility.
stripchart.tcl Tcl/Tk history/ODB data stripchart display.
mspeaker, mlxspeaker Message speech synthesizer.
mcnaf CAMAC utility.
lazylogger Multi channel background data copier.
mevb Event Builder.
Provide user access to the Midas system for data storing and retrieval, experiment configuration and
monitoring as well as debugging tools.
analyzer Online / offline analyzer.
mhttpd Web server.
melog Electronic LogBook utility.
mtape Tape utility.
hvedit task HV or Slow control Windows/Qt application.
Documented on: midas.psi.ch
Reviewed in the following sides & documented on: midas.psi.ch
Notes: Essential tools for a proper acquisition system are available. Ranging from data monitoring/diagnostic to web interface. The first section of utility application are reviewed during this course, while from the second section “odbedit”, “analyzer” have been covered during the first part of the course, the other are just mentioned. Refer to the documentation for more details.

## Slide 10
odbedit
Online database Editor.
C:\>odbedit
[local:midas:S]/>help
Database commands ([] are options, <> are placeholders):
alarm - reset all alarms
cd <dir> - change current directory
chat - enter chat mode
chmod <mode> <key> - change access mode of a key
1=read | 2=write | 4=delete
cleanup [clientname] - delete hanging clients
copy <src> <dest> - copy a subtree to a new location
create <type> <key> - create a key of a certain type
create <type> <key>[n] - create an array of size [n]
del/rm [-l] [-f] <key> - delete a key and its subkeys
-l follow links
-f force deletion without asking
exec <key>/<cmd> - execute shell command (stored in key) on server
exp <key> <filename> - import key into ASCII file
find <pattern> - find a key with wildcard pattern
help/? [command] - print this help [for a specific command]
hi [analyzer] [id] - tell analyzer to clear histos
imp <filename> [key] - import ASCII file into string key
ln <source> <linkname> - create a link to <source> key
load <file> - load database from .ODB file at current position
- hit return for more --
ls/dir [-lhvrp] [<pat>] - show database entries which match pattern
-l ,-h, -v, -r, -p - See online help
make [analyzer name] - create experim.h
mem [-v] - show memeory usage [verbose]
mkdir <subdir> - make new <subdir>
move <key> [top/bottom/[n]] - move key to position in keylist
msg [type] [user] <msg> - compose user message
old [n] - display old n messages
passwd - change MIDAS password
pause - pause current run
scl [-w] - show all active clients [with watchdog info]
shutdown <client>/all - shutdown individual or all clients
sor - show open records in current subtree
start [number][now][-v] - start a run [with a specific number],
[now] w/o asking parameters, [-v] debug output
stop [-v] - stop current run, [-v] debug output
trunc <key> <index> - truncate key to [index] values
ver - show MIDAS library version
webpasswd - change WWW password for mhttpd
wait <key> - wait for key to get modified
quit/exit - exit
Main application for interaction with the Online Database.
Implements most of the midas functions.
Run control (start/stop)
Shell (recall, tab completion)
Command line (odbedit –c …)

## Slide 11
dio
/* Grant access to the device's ioports */
iopl() // change I/O privilege level
File: start_dragon04_fe
#!/bin/csh
/usr/local/bin/dio fedragon -e dragon -h dragon04.triumf.ca
Application launcher meant to give to the program privileges for I/O port access. Overcome the necessity
to have specific OS driver for each interface.
By accessing directly the IO ports, the launched program has full R/W access to IO port. Device access through that port is faster, but multiple instance of such task running simultaneously may generate IO collision resulting in wrong data transfer to bus timeout.
Application launcher for Direct IO access.
Dragon
Notes: Direct I/O application launcher to allow unrestricted access to the I/O port from within the application. Used for CAMAC/VME access through the ISA, PCI port.

## Slide 12
Equipment
listing
Logger
channel
Client
listing
Run
Info
Odb>ls /Runinfo
Odb>ls /Experiment
Odb>ls /Equipment
Odb>ls /Logger
Odb>ls /System
Odb>ls /Programs
mstat
Status display.
Midas ASCII status display (VT100 display). Precursor of the Web interface.
The data are retrieved from the different ODB locations.
*-v1.8.0- MIDAS status page -------------------------Mon Apr 3 11:52:52 2000-*
Experiment:chaos Run#:8699 State:Running Run time :00:11:34
Start time:Mon Apr 3 11:41:18 2000
FE Equip. Node Event Taken Event Rate[/s] Data Rate[Kb/s]
B12Y pcch02 67 0.0 0.0
CUM_Scaler vwchaos 23 0.2 0.2
CHV pcch02 68 0.0 0.0
KOS_Scalers vwchaos 330 0.4 0.6
KOS_Trigger vwchaos 434226 652.4 408.3
KOS_File vwchaos 0 0.0 0.0
Target pcch02 66 0.0 0.0
Logger Data dir: /scr0/spring2000 Message File: midas.log
Chan. Active Type Filename Events Taken KBytes Taken
0 Yes Disk run08699.ybs 434206 4.24e+06
Lazy Label Progress File name #files Total
cni-53 100[%] run08696.ybs 15 44.3[%]
Clients: MStatus/koslx0 Logger/koslx0 Lazy_Tape/koslx0
CHV/pcch02 MChart1/umelba ODBEdit/koslx0
CHAOS/vwchaos ecl/koslx0 Speaker/koslx0
MChart/umelba targetFE/pcch02 HV_MONITOR/umelba
SUSIYBOS/koslx0 History/kosal2 MStatus1/dasdevpc
*------------------------------------------------------------------------------*
Lazy
logger
Odb>ls /Lazy
CHAOS
Notes: Basic status of a Midas experiment. The display summarize the status of the different element of the Data acquisition system.

## Slide 13
mdump
Mon> mdump -e tigress -h midtig01 -f d | more
-1.9.1 -- Enter <!> to Exit ------- Midas Dump ---
------------------------ Event# 1 ------------------------
Evid:0001- Mask:0000- Serial:7439022- Time:0x3eb695af- Dsize:19840/0x4d80
#banks:18 - Bank list:-POSIDGF1SIA0SIA1SIA2SIA3SIA4SIA5SIA6SIA7SIB0SIB1SIB2SIB3S
IB4SIB5SIB6SIB7-
Bank:POSI Length: 8(I*1)/2(I*4)/2(Type) Type:Real*4 (FMT machine dependent)
1-> 0.000e+00 0.000e+00
Bank:DGF1 Length: 3290(I*1)/822(I*4)/1645(Type) Type:Unsigned Integer*2
1-> 1645 1 4352 1299 33320 34813 15 33320
9-> 37430 409 44557 7297 18692 0 0 0
17-> 0 1299 6100 6100 6060 6008 6072 6104
25-> 6076 6048 6040 6068 6088 6048 6032 6068
33-> 6084 6072 5988 5956 5948 5936 6048 6136
41-> 6120 6120 6152 6176 6116 6024 6012 6032
49-> 6064 6088 6228 6204 6136 6180 6176 6172
57-> 6156 6056 6004 6012 5988 6000 6088 6172
65-> 6180 6140 6160 6156 6168 6144 6136 6088
73-> 6096 6104 6148 6084 6008 5996 6004 6024
81-> 6072 6020 6064 6136 6120 6108 6080 6032
Debugging application: allow to display the events (banks) during acquisition or from a save-set file (file.mid)
Meant for debugging and data consistency check. mdump displays the “bank” data.
Sun> mdump -e tigress -h midtig01 -s
…
Level: 98.468 %, Rate: 0.000 MB/sec
Level: 98.468 %, Rate: 1.043 MB/sec
Level: 98.468 %, Rate: 1.099 MB/sec
Level: 98.472 %, Rate: 1.112 MB/sec
Level: 98.155 %, Rate: 1.101 MB/sec
…
Sun> mdump -e tigress -h midtig01 -y
Last - Evid:0000- Mask:0000- Serial:0- Time:0x0- Dsize:0/0x0
Now - Evid:0001- Mask:0000- Serial:3358866- Time:0x3eb58317- Dsize:19840/0x4d80
Consistency check: \ - 3358882
Last - Evid:0001- Mask:0000- Serial:3358882- Time:0x3eb58317- Dsize:19840/0x4d80
Now - Evid:0002- Mask:0001- Serial:10811- Time:0x3eb58318- Dsize:24/0x18
Event display utility
Tigress
Notes: Event dump utility for capturing the event as they migrate from the frontend to the backend server. In practice “mdump” is a Midas client as any other task connected to the experiment. “mdump” looks essentially to the “event buffer” to get its data.

## Slide 14
mlogger
Multi channel Data logger and history data collector I.
History available as soon as Logger running.
History definition re-scanned @ BOR.
Channel Setting re-scanned @ BOR.
History works on Event ID only.
ODB
SYSMSG
SYSTEM
BUF1
Midas Buffers
BUF2
mlogger provides 3 main services to the Midas experiment.
Centralize system message logging (log file).
Multiple Data logging channel (logger/channels/<0>, <1>, …).
History data logging (Frontend defined, /History/links).
ODB Dump
ODB Dump file
Run Level
History
date.hst
History definition
re-scanned
ODB dump
Run#.odb
ODB dump
MIDAS
.mid
DUMP
.???
ASCII
.ascii
ROOT
.root
ODB dump
ODB dump
YBOS
.ybs
ODB dump
msg
Tape
Disk
/Logger/Channels/1
Event ID & Trig. Mask
ODB Dump = N
Data Type = ROOT
Buffer = BUF1
Log Message = 0
Type = Disk
FTP
Application Level
History
date.hst
Log
midas.log
History definition
Scan
Append entries
Channels Level
ODB dump
MIDAS
.mid
DUMP
.???
ASCII
.ascii
ROOT
.root
ODB dump
ODB dump
YBOS
.ybs
ODB dump
msg
Tape
FTP
/Logger/Channels/0
Event ID & Trig. Mask
ODB Dump = Y
Data Type = MIDAS
Buffer = SYSTEM
Log Message = 1
Type = Disk
Disk
Notes: Application for storing the collected data. Multiple data format are available (MIDAS, YBOS, ROOT).

## Slide 15
mlogger
Multi channel Data logger and history data collector II.
[ltno01:ltno:Running]/>ls -lr /Logger/
Key name Type #Val Size Last Opn Mode Value
-----------------------------------------------------------------------
Logger DIR
Data dir STRING 1 256 87h 0 RWD /data1/ltno
Message file STRING 1 256 87h 0 RWD midas.log
Auto restart BOOL 1 4 87h 0 RWD n
Write data BOOL 1 4 87h 0 RWD y
ODB Dump BOOL 1 4 87h 0 RWD n
Tape message BOOL 1 4 87h 0 RWD y
ODB Dump File STRING 1 256 87h 0 RWD run%05d.odb
channels DIR
0 DIR
Settings DIR
Active BOOL 1 4 7m 0 RWD y
Type STRING 1 8 7m 0 RWD Disk
Filename STRING 1 256 7m 0 RWD run%05d.mid
Format STRING 1 8 7m 0 RWD MIDAS
ODB dump BOOL 1 4 7m 0 RWD y
Log messages DWORD 1 4 7m 0 RWD 0
Buffer STRING 1 32 7m 0 RWD SYSTEM
Event ID INT 1 4 7m 0 RWD -1
Trigger mask INT 1 4 7m 0 RWD 1
Event limit DWORD 1 4 7m 0 RWD 0
Byte limit DOUBLE 1 8 7m 0 RWD 0
Tape capacity DOUBLE 1 8 7m 0 RWD 0
Subdir format STRING 1 32 7m 0 RWD %Y%m%d
Current filename STRING 1 256 7m 0 RWD 20030504/run82104.mid
Statistics DIR
Events written DOUBLE 1 8 4s 0 RWDE 210
Bytes written DOUBLE 1 8 4s 0 RWDE 67795
Bytes written to DOUBLE 1 8 4s 0 RWDE 1.21489e+10
Files written INT 1 4 4s 0 RWDE 42616
Default destination directory
Subdirectory destination using
Coordinated Universal Time.
(man date)
Run control condition based on limits
Event ID Request : -1 => ALL
Trigger Mask Request : -1 => ALL
Data file template: Run#####.mid
    Run#####.ybs
    Run#####.root
Data file Format: MIDAS, YBOS, ASCII, DUMP, ROOT
Default system log file name
Default Source buffer name
Global Logger flags
ODB ASCII dump file
Destination type: Disk, Tape, FTP
LTNO
Notes: Mlogger has several configuration options for each logging channel. All the parameters are available in the ODB.

## Slide 16
mhist
mhist -s 021118 -p 021228 -e 10 -t 7200 -v "Bell 5080 Gaussmeter Measured"
Nov 18 00:00:34 2002 -146.8
Nov 18 02:02:38 2002 -146.5
Nov 18 04:04:43 2002 -146.1
Nov 18 06:06:47 2002 -146.1
Nov 18 08:08:50 2002 -196
Nov 18 10:10:47 2002 -196
Nov 18 12:11:48 2002 -195.6
Nov 18 14:13:27 2002 -195.2
…
History data utility I.
Target Control
Tool for extracting history data from the save-set files.
History save-set files produced by the logger.
Can generate large quantity of data.
Daily file (031123.hst)
Easily exported (.xls)
TWIST
Notes: Mlogger has the task to record “history” data to file. These data can be retrieved later on by a dedicated application “mhist”. The output is formatted in such a way that simple piping to standard spreadsheet is possible.

## Slide 17
mchart -e ltno -c -f Gauss -q /equipment/meters/variables
 Files: Gauss.conf (configuration) , Gauss (data)
mchart -e ltno -f Gauss –gh
 Update file Gauss  stripchart can read the update Gauss file
mchart, stripchart.tcl
History data utility II.
ODB data formatter for stripchart utility. Aternative
history display based on the Gnome stripchart. Customized version
stripchart.tcl for online history data and history files.
LTNO
Notes: Independent application “mchart” provides a mean of chart log any value of the ODB in real time using gstripchart or dedicated application stripchart.tcl. Stripchart.tcl has also the possibility to chart graphically the “history” data recorded prviously by “mlogger”.

## Slide 18
mspeaker, mlxspeaker
Message speech synthesizer.
Client interface to speech synthesizer program. Initially fun application to have, lately very useful tool when
counting room gets too crowed .
Used for:
Triggered Odbedit msg or chat command.
Triggered by function call cm_msg(MUSER/MTALK,…).
Sun> odb -e chaos -h koslx0
[koslx0:chaos:Stopped]/>chat
Your name> Pierre
Exit chat mode with empty line.
> Is the chamber fixed yet?
09:27:55 [Pierre] Is the chamber fixed yet?
09:28:42 [Greg] Well, we're waiting for you!
cm_msg(MTALK, ”my_prg”, ”Spoken message”);
Example: mlogger.c
…
if (status != SS_SUCCESS && !stop_requested) {
if (status == SS_IO_ERROR)
cm_msg(MTALK, "log_write", "Physical IO error on %s, stopping run", log_chn->path);
else
cm_msg(MTALK, "log_write", "Error writing to %s, stopping run", log_chn->path);
stop_requested = TRUE;
cm_transition(TR_STOP, 0, NULL, 0, ASYNC, FALSE);
stop_requested = FALSE;
}
Sat> mlxspeaker -D
DEMO
Logger code
#!/bin/tcsh
# Script to restart all DAQ processes running on machine TWIST …
# The Midas text to audio processor
odb -c scl -e $expt | grep --silent -i speaker
if ( "$?" != "0" ) then
echo "Starting mlxspeaker as daemon"
mlxspeaker -e $expt -D \
-u 'play --volume=0.3 /home/twistonl/bin/wav/bleep8.wav‘ \
-t 'play --volume=0.4 /usr/share/sounds/KDE_Dialog_Appear.wav' -s 5&
endif
Sun> odb -e chaos -h koslx0
[koslx0:chaos:Stopped]/>msg “It’s too late, I’m going home”
TWIST
mspeaker W2k
mlxspeaker Linux
FirstByte/ProVoice
Festival
sysmsg
Is the chamber
fixed yet?
Notes: Interface to a Voice synthesizer program. Allows Midas program client as well as user (through odb>chat, odb>msg) to send messages to be spoken.

## Slide 19
E823 [/home/e823/online]>mcnaf
mCNAF> [B0C0N01A02F00 [0/0x000000 Q0X0] R1W0M24] :c1n13a0f0
mCNAF> [B0C1N13A00F00 [1/0x000001 Q1X1] R1W0M24] :n19
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R1W0M24] :
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R1W0M24] :r3 Repeat
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R3W0M24] :g Go
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R3W0M24] <-001
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R3W0M24] <-002
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R3W0M24] <-003
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R3W0M24] :w100 Wait
mCNAF> [B0C1N19A00F00 [252/0x0000fc Q1X1] R3W100M24] :j Job
mCNAF> Job file name [cnaf.cnf]:rewind
mCNAF> [B0C1N30A09F24 [252/0x0000fc Q1X1] R3W100M24]
mCNAF> [B0C1N13A00F09 [0/0x000000 Q1X1] R3W100M24]
mCNAF> [B0C1N13A00F16 [6/0x000006 Q1X1] R3W100M24]
Interactive program for access to CAMAC system, essential for debugging.
Repeat, Delay, 16/24bit.
Submit Job.
CNAF calls
Midas CAMAC Standard (mcstd.h)
CAMAC utility.
mcnaf
/midas/utils/makefile.mcnaf: Build mcnaf, miocnaf, (mdrvcnaf)
Sun> dio miocnaf  mcnaf with Direct IO access without Frontend
Sun> mdrvcnaf  mcnaf with proper driver without Frontend (lxcamac)
Sun> mcnaf  mcnaf through frontend (RPC)
E823 [/home/e823/online]>more rewind
c1n30a9f24
n13f9a0
f16x006
f16x806
f16x006
f16x000
x0
x0
f9a0
f16a1d0
d10000
d10000000
d10110000
d10210000
xffffff
f9a0
f26a1
a2
E823
Hardware supported:
KCS2926, KCS2927 (dio/lx)
DSP004(dio)
HYT1331(dio)/w2k/lx
WIENER-CC32(w2k/lx)
JORWAY73A(lx)
CES8210(vxWorks)
Address
Data Dec/Hex
QX
Wait
Repeat
Mode
Notes: Simple CNAF interactive program for gaining access to CAMAC. This interface works with any type of CAMAC hardware as long that mcstd calls are used in the bus driver.

## Slide 20
DISK STORAGE AREA
Background Multi channel data copier I.
lazylogger
Application meant to decouple the acquisition from the actual streamer data storing task.
Fed up with 8mm tapes.
The tape handling of the streamer device requires(ed) lengthy initialization operation [8mm Tape] which impacts on the experimenter patience and acquisition live time in particular for short run time.
Time line
Time line
ODB
/Lazy/Disk/Settings/List Label = TAPE193
/Lazy/Disk/Settings/List/TAPE193[ ]
43
44
45
46
Stay behind = 2
Stay behind = -2
Start from 2 behind
Start from the oldest up to 2 behind
DISK_recover.odb
After each backup
/Lazy tree is saved
Run
00043
.mid
Run
00044
.mid
Run
00045
.mid
Run
00046
.mid
Run
00048
.mid
Run
00049
.mid
Run
00051
.mid
Run
00047
.mid
Run
00050
.mid
DAQ
Tape
FTP
/alias/max_rate < 200
YES
Disk
.mid
Backup Type = Disk
LazyLogger
ALWAYS
NEVER
Condition
Running
condition
File 43
To Trashcan
Entry 43 in
TAPE193[ ]
removed
YES
43 in TAPE193[ ] list
&&
Maintain Free Space
Space <
Notes: Decoupling application between the DAQ and the data storage. Was a benefit in previous experiments where 8mm SCSI streamer tape were used. Now-a-days DLT are “fast” enough, but lazylogger provides a delay between the acquisition and the storage which can be used for fast replay of the disk file.

## Slide 21
[/Lazy/Tape/Settings]
Maintain free space(%) = INT : 15
Stay behind = INT : -1
Alarm Class = STRING : [32] Warning
Running condition = STRING : [128] ALWAYS
Data dir = STRING : [256] /data_onl/current
Data format = STRING : [8] YBOS
Filename format = STRING : [128] run%05d.ybs
Backup type = STRING : [8] Tape
Execute after rewind = STRING : [64] /home/twistonl/online/bin/ask_for_tape.sh
Path = STRING : [128] /dev/nst0
Capacity (Bytes) = FLOAT : 5e+10
List label = STRING : [128] tw0166
Execute before writing file = STRING : [64] /home/twistonl/online/bin/lazy_prewrite.csh
Execute after writing file = STRING : [64] /home/twistonl/online/bin/rundb_addrun.pl
Modulo.Position = STRING : [8] 1.0
Tape Data Append = BOOL : y
[/Lazy/Tape/Statistics]
Backup file = STRING : [128] run06746.ybs
File size [Bytes] = FLOAT : 2.00347e+09
KBytes copied = FLOAT : 2.00347e+09
Total Bytes copied = FLOAT : 2.98002e+10
Copy progress [%] = FLOAT : 100
Copy Rate [bytes per s] = FLOAT : 1.73682e+06
Backup status [%] = FLOAT : 99.334
Number of Files = INT : 21
Current Lazy run = INT : 6746
[/Lazy/Tape/List]
tw0153 = INT : 9108
tw0154 = INT[71] :
[0] 9109
[1] 9110
[2] 9111
[3] 9112
[4] 9113
[5] 9114
Background Multi channel data copier II.
lazylogger
Keep the drive with a minimum of %GB
Stay behind… leave always 1 full run on the disk between the lazy run and the current run.
Data source directory
For multiple lazylogger channel on the
same data source (3.1, 3.2, 3.3)
Data Format: MIDAS, YBOS
Once a run has been backed up, the run number appear in the List tree. It will remain in the list until the physical source file is removed from the source directory (Space maintenance).
Mon May 20 15:09:13 2002 [Lazy_Tape] tw0058[1] (cp:125.5s) /dev/nst0/run04390.ybs 530.156MB file NEW (total 16966 blocks)
Mon May 20 15:09:24 2002 [Lazy_Tape] Starting lazy job on run04391.ybs
Mon May 20 15:16:02 2002 [Lazy_Tape] tw0058[2] (cp:397.8s) /dev/nst0/run04391.ybs 1908.438MB file NEW (total 78037 blocks)
Mon May 20 15:16:12 2002 [Lazy_Tape] Starting lazy job on run04392.ybs
Midas.log
Label of the backup tape
TWIST
TWIST
Destination type : Tape, Disk, FTP
Notes: Multiple instance of “lazylogger” can be started. Each instance having different destination storage (DISK, TAPE, FTP).

## Slide 22
eb_begin_of_run(int run, char *UserField, char *error )
eb_end_of_run(int run, char *error )
All Frag
Poll event[frag]i
Compose Event Header
eb_user(*fragi , *dest., …)
User Build?
Assemble Destination Event
Send Dest. event
Incomplete
Error
Complete
All fragments in
Check Serial numbers
eb_user(INT nfrag
, EBUILDER_CHANNEL * ebch
, EVENT_HEADER *pheader
, void *pevent
, INT *dest_size)
ODB structure
Event source A
TWIST (poster RT-122)
On 2xPIII-1.2GHz/1GB – 2xIDE100
ETH0 - FE-source1 12% 3.5MB/s
ETH1 - FE-source2 12% 3.5MB/s
Mevb 15%
Mlogger 20% 7.0MB/s
[midtwist:twist:Stopped]/EBuilder>ls –lr
Key name Type #Val Size Last Opn Mode Value
--------------------------------------------------------------------
EBuilder DIR
Settings DIR
Event ID WORD 1 2 >99d 0 RWD 1
Trigger mask WORD 1 2 >99d 0 RWD 1
Buffer STRING 1 32 >99d 0 RWD SYSTEM
Format STRING 1 32 >99d 0 RWD YBOS
User Field STRING 1 64 >99d 0 RWD 100
Event mask WORD 1 4 >99d 0 RWD 3
User_build BOOL 1 4 >99d 0 RWD n
hostname STRING 1 64 14h 0 RWD midtwist
Statistics DIR
Events sent DOUBLE 1 8 9h 0 RWD 0
Events per sec. DOUBLE 1 8 9h 0 RWD 0
kBytes per sec. DOUBLE 1 8 9h 0 RWD 0
Channels DIR
Frag1 DIR
Settings DIR
Event ID WORD 1 2 >99d 0 RWD 1
Trigger mask WORD 1 2 >99d 0 RWD 65535
Buffer STRING 1 32 >99d 0 RWD YBUF1
Format STRING 1 32 >99d 0 RWD YBOS
Event mask DWORD 1 4 >99d 0 RWD 1
Statistics DIR
Events sent DOUBLE 1 8 87h 0 RWD 227392
Events per sec. DOUBLE 1 8 87h 0 RWD 224696
kBytes per sec. DOUBLE 1 8 87h 0 RWD 0
Frag2 DIR
Settings DIR
Event ID WORD 1 2 >99d 0 RWD 5
Trigger mask WORD 1 2 >99d 0 RWD 65535
Buffer STRING 1 32 >99d 0 RWD YBUF2
Format STRING 1 32 >99d 0 RWD YBOS
Event mask DWORD 1 4 >99d 0 RWD 2
Statistics DIR
Events sent DOUBLE 1 8 87h 0 RWD 227393
Events per sec. DOUBLE 1 8 87h 0 RWD 224697
kBytes per sec. DOUBLE 1 8 87h 0 RWD 0
Event Setting
Fragment 1
Event Setting
Fragment 2
source_scan()
TWIST
EVTID=1
Serial number (1)
Time Stamp
Event Data Size (bytes)
Trig.Msk=-1
EVTID=5
Serial number (1)
Time Stamp
Event Data Size (bytes)
Trig.Msk=-1
Event source B
EB event
insertion
bitwise
Event Setting
Composition
EVTID=1
Serial number (1)
Time Stamp
Event Data Size (bytes)
Trig.Msk=1
mevb
Event Builder.
Notes: The event builder collects data from multiple source buffer, assembles them based on the “serial number” criteria and send them to the destination buffer. User hook is available in the sequence for monitoring the traffic.

## Slide 23
Features & Hidden Features
In the Frontend
Manual Trigger Enable manual trigger of the equipment.
Large Event Allow large event collection.
Tiny Event Allow small event packing.
Deferred transition Allow transition operation based on condition.
Multiple Equipment/
frontend_loop() Code examples
In the ODB
Edit on Start Allow specific run parameters entries at BOR.
Parameter Comments Specify comment for Run start with Web browser
Lock when running Allow ODB variables write protect during run.
Security Control Midas experiment access (ODB, tasks).
History dir Specify History dir.
Elog dir Specify Elog dir.
In the Web Browser
Alias Shortcut hyperlink.
Script Script hyperlink.
Custom Custom Midas web page.
Most of the Midas features become available once the particular application implementing this feature is started.
Ex: “mlogger” task will create a default structure in the ODB to match its requirements.
The user has the possibility to modify the values and have “immediate reasoned effect”.
Some features are not directly related to an application but address more a behavior of the system. In these cases
the user has to activate such a “hidden feature” by a particular action (I.e: creation of an entry in ODB).
Notes: While standard applications are available from the distribution, there are several features that don’t come noticeable without specific activation. These features applies to the “frontend” , “ODB”, and the “Midas Web status“.

## Slide 24
Midas features driven by the experiment requirements I
fev680
VxWorks
Darc
files
µSR _config
µSRrc
MIDAS
Event
Please!
------------------------ Event# 14 ------------------------
Evid:0003- Mask:0000- Serial:1327- Time:0x3ebbdd33- Dsize:80/0x50
#banks:1 Bank list:-SCLR-
------------------------ Event# 15 ------------------------
Evid:0003- Mask:0000- Serial:1328- Time:0x3ebbdd38- Dsize:80/0x50
#banks:1 Bank list:-SCLR-
------------------------ Event# 16 ------------------------
Evid:0002- Mask:0000- Serial:43- Time:0x3ebbdd39- Dsize:4096068/0x3e8044
#banks:5 Bank list:-HI00HI01HI02HI03HI04-
------------------------ Event# 17 ------------------------
Evid:0003- Mask:0000- Serial:1329- Time:0x3ebbdd41- Dsize:80/0x50
#banks:1 Bank list:-SCLR-
------------------------ Event# 18 ------------------------
Evid:0003- Mask:0000- Serial:1330- Time:0x3ebbdd47- Dsize:80/0x50
#banks:1 Bank list:-SCLR-
µSR
µSR experiment
Uses special VME TDC (V680) hardware.
Build large size internal histograms in the Frontend.
Requires flexible re-configuration between runs.
Simple interface to the µSR standard data format.
Event request on demand (mdarc).
mDARC
Notes: As previously mentioned the main driving force for improvement comes from the user requests. MuSr has been a player by asking Midas to provide the tools implemented in their previous DAQ system running under VMS. “Manual Trigger”, “Large Event”, “Scripts” are some of them.

## Slide 25
C:\>mdump -f x
-1.9.1 -- Enter <!> to Exit ------- Midas Dump ---
------------------------ Event# 1 ------------------------
Evid:0003- Mask:0000- Serial:17- Time:0x3e9b89c1- Dsize:4000020/0x3d0914
#banks:1 - Bank list:-BIGG-
Bank:BIGG Length: 4000000(I*1)/1000000(I*4)/1000000(Type) Type:Integer*4
1-> 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000
9-> 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000
17-> 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000 0x00000000
25-> 0x00000000 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd
33-> 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd
…
999937-> 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd
999945-> 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd
999953-> 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd
999961-> 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd
999969-> 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xcdcdcdcd 0xffffffff
999977-> 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff
999985-> 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff
999993-> 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff 0xffffffff
Frontend: Huge Event
Transmit event larger than default frontend
buffer size.
File : hugefe.c
Comment: Event sent individually. No buffering.
INT read_huge_event(char *pevent, INT off)
{
DWORD *pddata;
/* init bank structure */
bk_init32(pevent);
bk_create(pevent, "BIGG", TID_DWORD, &pddata);
…
pddata += 1000000;
bk_close(pevent, pddata);
return bk_size(pevent);
}
/* maximum event size for fragmented events (EQ_FRAGMENTED) */
INT max_event_size_frag = 5*1024*1024;
{ “Huge", /* equipment name */
2, 0, /* event ID, trigger mask */
"SYSTEM", /* event buffer */
EQ_PERIODIC | EQ_FRAGMENTED, /* equipment type */
0, /* event source */
"MIDAS", /* format */
TRUE, /* enabled */
RO_RUNNING | /* read when running */
RO_TRANSITIONS | /* and on transitions */
RO_ODB, /* and update ODB */
10000, /* read every 10 sec */
0, /* stop run after this #evts */
0, /* number of sub events */
0, /* log history */
"", "", "",
read_huge_event, /* readout routine */
},
…
Equipment structure
readout function
Result
Booked 5MB used 4MB
DEMO /µSR

## Slide 26
{ “mantrig", /*equipment name */
2, 0, /* event ID, trigger mask */
"SYSTEM", /* event buffer */
EQ_PERIODIC |
EQ_MANUAL_TRIG, /* equipment type */
0, /* event source */
"MIDAS", /* format */
TRUE, /* enabled */
RO_RUNNING |
RO_TRANSITIONS | /* read when running and on transitions */
RO_ODB, /* and update ODB */
10000, /* read every 10 sec */
0, /* stop run after this event limit */
0, /* number of sub events */
0, /* log history */
"", "", "",
read_mantrig_event, /* readout routine */
},
Frontend: Manual Trigger
Enable “Manual Trigger” button in the Web browser Midas page. Requested by user to force special computation/statistics done in an equipment.
File : mantrigfe.c
Equipment structure
…
status = cm_connect_client(fe_name, &hconn);
if (status != RPC_SUCCESS) {
…
}
else {
status = rpc_client_call(hconn, RPC_MANUAL_TRIG, event_id);
if (status != CM_SUCCESS) {
…
cm_disconnect_client(hconn, FALSE);
}
}
…
DEMO/µSR
mhttpd /µSR
Result

## Slide 27
Midas features driven by the experiment requirements II
GPS experiments (Precise Half-Life Measurements).
Uses dedicated radioactive ions tape transport.
Needs tape mechanism control synchronized with the DAQ.
Measurement cycle can be long, ensure data validity over the full run.
Tape movement constrain (keep it moving!).
Secondary equipment for Ge LAM data collection.
Synchronize LifeTime cycle with primary beam (EPICS).
Sequencer
MSC
Ge ADC
Ion implantation
4pi Detector
Notes: Another driving force experiment has been GPS (E823) where control of their target mechanism and synchronization to the DAQ was a necessity, required the implementation of specific features. “Deferred transition”, “tiny event”, Epics interface for acquisition synchronization with the beam production.

## Slide 28
Frontend: Deferred transition I
Postpone transition until user condition satisfied.
TR_STOP : Wait for final cycle, start Bg tape move.
TR_START: Initialize sequencer, stop Bg tape move.
.mid
files
Lifetime FE
Eqp: MCS
Eqp: GE
NOVA
analyzer
MIDAS
BOR:
Move Tape.
Initialize sequence.
Acquisition:
Wait for implantation
Move Tape to 4pi counter
Start decay measurement
Collect decay data (MSC)
Move Tape
…
Frontend_loop()
Keep Tape moving
Cycle
Notes: Allows proper starting/ending of acquisition cycle.

## Slide 29
Frontend: Deferred transition II
INT read_deferred_event(char *pevent, INT off)
{
DWORD *pdata;
bk_init(pevent);
bk_create(pevent, “DEFR", TID_DWORD, &pdata);
…
bk_close(pevent, pdata);
if (transition_PS_requested) {
// transition acknowledged, but...
// carry on until hardware condition satisfied
// ...
if (pseudo_delay++ < 3) {
// Ignore transition
printf("Transition ignored, ");
} else {
// Time to do transition
printf("End of cycle... perform transition\n");
end_of_mcs_cycle = TRUE;
}
}
printf("Event ID:%d - Event#: %d\n", EVENT_ID(pevent), SERIAL_NUMBER(pevent));
return bk_size(pevent);
}
readout function
File : deferredfe.c
Comments:
Only for Polled Equipment.
Register for specific Transition (START, PAUSE,
RESUME, STOP)
Event buffer size : 100000
Buffer allocation : 2 x 100000
System max event size : 524288
User max event size : 10000
User max frag. size : 5242880
# of events per buffer : 10
Event ID:2 - Event#: 1
Event ID:2 - Event#: 2
Event ID:2 - Event#: 3
Transition requested...
Transition ignored, Event ID:2 - Event#: 4
Transition ignored, Event ID:2 - Event#: 5
Transition ignored, Event ID:2 - Event#: 6
End of cycle... perform transition
Event ID:2 - Event#: 7
Run #21 stopped
Stop or pause requested
Result
BOOL transition_PS_requested = FALSE;
BOOL end_of_cycle = FALSE;
//-- Deferred transition callback
BOOL wait_end_cycle(int transition, BOOL first)
{
if (first) {
// Get there as soon as transition is requested
transition_PS_requested = TRUE;
printf("Transition requested...\n");
// Defer the transition now
return FALSE;
}
// Check user flag
if (end_of_cycle) {
// User flag set, ready to perform deferred transition now
transition_PS_requested = FALSE;
end_of_cycle = FALSE;
return TRUE;
}
else {
return FALSE; // User not ready for transition, defers it...
}
}
Declaration section
Callback function
INT frontend_init()
{
// register for deferred transition
cm_register_deferred_transition(TR_STOP, wait_end_cycle);
cm_register_deferred_transition(TR_PAUSE, wait_end_cycle);
…
Initialization function
DEMO/E823
Notes: Entire implementation of the “deferred transition” done in the frontend code.

## Slide 30
Frontend: Tiny Event
{ “Tiny", /* equipment name */
3, 0, /* event ID, trigger mask */
"SYSTEM", /* event buffer */
EQ_POLLED, /* equipment type */
1, /* event source */
"MIDAS", /* format */
TRUE, /* enabled */
RO_RUNNING | /* read when running */
RO_TRANSITIONS, /* and on transitions */
500, /* polling 500ms */
0, /* stop run after x events */
10, /* number of sub events */
0, /* log history */
"", "", "",
read_tiny_event, /* readout routine */
},
#define NWORDS 3
INT read_tiny_event(char *pevent, INT offset)
{
static WORD *pdata=NULL;
static WORD sub_counter=0;
// Super event structure
if (offset == 0) { // FIRST event of the Super event
bk_init(pevent);
bk_create(pevent, "SUPR", TID_WORD, &pdata);
sub_counter = 1;
}
else if (offset == -1) { // CLOSE Super event
bk_close(pevent, pdata);
return bk_size(pevent);
}
// READ event
*pdata++ = 0xB0E;
*pdata++ = sub_counter++;
*pdata++ = 0xE0E;
if (offset == 0) {
// Compute the proper event length on the FIRST pass
// sizeof(WORD) is defined by the TID_WORD in bk_create()
return NWORDS * sizeof(WORD)
+ sizeof(BANK_HEADER)
+ sizeof(BANK);
}
else {
// Return the data section size only
// sizeof(WORD) is defined by the TID_WORD in bk_create()
return NWORDS * sizeof(WORD);
}
…
Equipment structure
readout function
Transmit packed event under one bank. When the event data size is comparable to the header, packing multiple frontend events under a single bank improves CPU and disk usage. Requires proper sub-event handling at the analyzer level.
File : tinyfe.c
Comments: Only for Polled event
NWORDS * sizeof(WORD) * 10
C:\>mdump
-1.9.1 -- Enter <!> to Exit ------- Midas Dump ---
------------------------ Event# 1 ------------------------
Evid:0003- Mask:0000- Serial:12652821- Time:0x3e9b8207- Dsize:80/0x50
#banks:1 - Bank list:-SUPR-
Bank:SUPR Length: 60(I*1)/15(I*4)/30(Type) Type:Unsigned Integer*2
1-> 0x0b0e 0x0001 0x0e0e 0x0b0e 0x0002 0x0e0e 0x0b0e 0x0003
9-> 0x0e0e 0x0b0e 0x0004 0x0e0e 0x0b0e 0x0005 0x0e0e 0x0b0e
17-> 0x0006 0x0e0e 0x0b0e 0x0007 0x0e0e 0x0b0e 0x0008 0x0e0e
25-> 0x0b0e 0x0009 0x0e0e 0x0b0e 0x000a 0x0e0e
Result
DEMO/E823
Notes: Disk space and processor speed has not been always cheap or regular items. Running a full acquisition (hardware access, data collection, logging, analysis, display) on a single processor introduce unwanted dead time. In order to reduce this effect, in the case of short event collection, multiple events are gathered under the same bank which remove the header composition and the extra data transfer. It save disk space as well. The current alternative to the use of such feature is the use of dual fast processor or separated frontend node and dead cheap disk drive.

## Slide 31
Frontend: multiple polling equipment, frontend_loop()
/*-- Equipment list ----------------------------------------------*/
EQUIPMENT equipment[] = {
{ "MCS", /* equipment name */
1, 0x0001, /* event ID, trigger mask */
"SYSTEM", /* event buffer */
EQ_POLLED, /* equipment type */
LAM_SOURCE(CRATE, LAM_STATION(JW_N)), /* event source */
"MIDAS", /* format */
TRUE, /* enabled */
RO_RUNNING, /* read only when running */
5, /* poll for 5ms */
0, /* stop run after this event limit */
0, /* number of sub event */
0, /* don’t log history */
"", "", "",
read_mcs_event, /* readout routine */
},
{ "GE", /* equipment name */
2, 0x0002, /* event ID, trigger mask */
"SYSTEM", /* event buffer */
EQ_POLLED, /* equipment type */
LAM_SOURCE(CRATE, LAM_STATION(AD_N)), /* event source */
"MIDAS", /* format */
TRUE, /* enabled */
RO_RUNNING, /* read only when running */
100, /* poll for 100ms */
0, /* stop run after this event limit */
0, /* number of sub event */
0, /* don't log history */
"", "", "",
read_ge_event, /* readout routine */
},
{ "Scaler", /* equipment name */
4, 0x4, /* event ID, trigger mask */
"SYSTEM", /* event buffer */
EQ_PERIODIC, /* equipment type */
0, /* event source */
"MIDAS", /* format */
FALSE, /* disabled */
RO_RUNNING |
RO_TRANSITIONS | /* read when running and on transitions */
RO_ODB, /* and update ODB */
10000, /* read every 10 sec */
0, /* stop run after this event limit */
0, /* number of sub event */
0, /* log history */
"", "", "",
read_scaler_event, /* readout routine */
},
{ "" }
};
E823
/*-- Frontend Loop -------------------------------------------------*/
INT frontend_loop()
{
DWORD cur_time;
/* if frontend_call_loop is true, this routine gets called when
the frontend is idle or once between every event */
/* prepare sequencer */
static char bars[] = "|/-\\";
static int i_bar=0;
if ((i_bar++ % 10) == 0) {
printf("%c\r", bars[i_bar++ % 4]);
fflush(stdout);
}
if ((run_state == STATE_PAUSED) && (pause_time != 0)) {
cur_time = ss_time();
if ( (cur_time-pause_time) > (INT) seq.tape.delay) {
/* ready for moving tape */
if (sequencer(SEQ_MOVE_TAPE) == SUCCESS) {
pause_time = cur_time;
return SUCCESS;
}
return FE_ERR_HW;
}
}
}
char *frontend_name = "lifetime";
char *frontend_file_name = __FILE__;
…
/* frontend_loop is called periodically if this var. is TRUE */
BOOL frontend_call_loop = TRUE;
/* a frontend status page is displayed with this freq. in ms */
INT display_period = 3000;
…
/* globals */
BOOL end_of_mcs_cycle = FALSE;
BOOL transition_PS_requested= FALSE;
/*-- Function declarations ----------------------------------*/
…
INT read_mcs_event(char *pevent, INT off);
INT read_ge_event(char *pevent, INT off);
INT read_scaler_event(char *pevent, INT off);
INT channel_cycle_loop(void);
INT time_cycle_loop(void);
INT sequencer(INT action);
INT re_arm_ge(void);
INT re_arm_cycle(void);
E823
E823

## Slide 32
Entire information is (can be) available in ODB.
Develop/extend single interface for control & monitoring.
Implement hidden
features to no
clutter the already
busy display.
Ease the experiment control ODB/Web
Camac panel
Equipment
panels
Midas Web Run Control
SC panels
History panel

## Slide 33
OdbEdit: /Experiment/Edit on Start (hidden)
[local:bnmr1:S]Edit on start>start
run_title : NbSe2 H=-112G 40K 55-85 KHz 300Hz AFG=10mV
experiment_number : 815
experimenter : wam
sample : NbSe2
orientation : c-axis
temperature : 40K
field : -112G
Write Data : y
Run number [40066]:
Result
Result
ODB structure
Provides run parameters entries at “Begin of run” (BOR).
Comment: Will be available only in the “Run Start” page of the Web Browser Midas page.
Run started from the Web Browser
Run started from ODB
[local:bnmr1:S]/>cd "Experiment/Edit on start/
[local:bnmr1:S]Edit on start>ls -l
Key name Type #Val Size Last Opn Mode Value
--------------------------------------------------------------------------
run_title STRING 1 88 5m 0 RWD NbSe2 H=-112G 40K 55-85 KHz 300Hz AFG=10mV
experiment_number DWORD 1 4 5m 0 RWD 815
experimenter STRING 1 32 5m 0 RWD wam
sample STRING 1 11 5m 0 RWD NbSe2
orientation STRING 1 11 5m 0 RWD c-axis
temperature STRING 1 11 5m 0 RWD 40K
field STRING 1 11 5m 0 RWD -112G
Write Data LINK 1 19 >99d 0 RWD /Logger/Write data
Edit run number BOOL 1 4 6h 0 RWD n
Bnmr
Not editable field

## Slide 34
[local:bnmr1:S]/Experiment>cd "Parameter Comments/
[local:bnmr1:S]Parameter Comments>ls -l
Key name Type #Val Size Last Opn Mode Value
---------------------------------------------------------------------------
experimenter STRING 1 35 1m 0 RWD <H2><b> Some useful name!</b></H2>
field STRING 1 32 1m 0 RWD <i>Not in Tesla!</i>
OdbEdit: /Experiment/Parameter Comments (hidden)
Provides additional run parameters comments for the Web browser form.
If parameters are not clear enough!
Comment: Will be only available in the “Run Start” page of the Web Browser Midas page.
ODB structure
Result
DEMO / Bnmr

## Slide 35
[local:bnmr1:S]/>cd "Experiment/Lock when running/
[local:bnmr1:S]Lock when running>ls -l
Key name Type #Val Size Last Opn Mode Value
---------------------------------------------------------------------------
dis_rn_check LINK 1 51 >99d 0 RWD /Equipment/FIFO_acq/mdarc/disable run number check
Input LINK 1 35 88h 0 RWD /Equipment/FIFO_acq/sis mcs/Input/
SIS test mode LINK 1 43 88h 0 RWD /Equipment/FIFO_acq/sis mcs/sis test mode/
SIS ref A LINK 1 65 88h 0 RWD /Equipment/FIFO_acq/sis mcs/Hardware/Enable SIS ref ch1 scaler A
SIS ref B LINK 1 65 88h 0 RWD /Equipment/FIFO_acq/sis mcs/Hardware/Enable SIS ref ch1 scaler B
[local:bnmr1:S]Lock when running>
OdbEdit: /Experiment/Lock when running (hidden)
[local:bnmr1:S]Hardware>ls -l
Key name Type #Val Size Last Opn Mode Value
------------------------------------------------------------------------
num cycles DWORD 1 4 18h 0 RWD 0
Fluor monitor thr DWORD 1 4 20h 0 RWD 0
Cycle thr (%) FLOAT 1 4 6h 0 RWD 20
Diagnostic channel num INT 1 4 20h 0 RWD 2
Re-reference BOOL 1 4 6h 0 RWD n
num polarization cycles DWORD 1 4 20h 0 RWD 0
polarization switch delay DWORD 1 4 20h 0 RWD 0
Enable SIS ref ch1 scaler A BOOL 1 4 20h 0 RWD n
Enable SIS ref ch1 scaler B BOOL 1 4 20h 0 RWD y
Enable helicity flipping BOOL 1 4 8h 0 RWD y
PPG acq cycle control BOOL 1 4 20h 0 RWD y
…
[local:bnmr1:S]Hardware>start now
Starting run #40066
23:13:25 [ODBEdit] Run #40066 started
[local:bnmr1:R]Hardware>ls -l
Key name Type #Val Size Last Opn Mode Value
------------------------------------------------------------------------
num cycles DWORD 1 4 18h 0 RWD 0
Fluor monitor thr DWORD 1 4 20h 0 RWD 0
Cycle thr (%) FLOAT 1 4 6h 0 RWD 20
Diagnostic channel num INT 1 4 20h 0 RWD 2
Re-reference BOOL 1 4 6h 0 RWD n
num polarization cycles DWORD 1 4 20h 0 RWD 0
polarization switch delay DWORD 1 4 20h 0 RWD 0
Enable SIS ref ch1 scaler A BOOL 1 4 20h 0 R n
Enable SIS ref ch1 scaler B BOOL 1 4 20h 0 R y
Enable helicity flipping BOOL 1 4 8h 0 RWD y
PPG acq cycle control BOOL 1 4 20h 0 RWD y
[local:bnmr1:R]Hardware>
[local:bnmr1:R]Hardware>set "Enable SIS ref ch1 scaler A" y
Write access not allowed
Run Stopped
Run in Progress
Starting run
Set Read Only access to declared ODB Variables when run in progress.
Useful to prevent user to change critical run parameters during data taking.
Result
ODB structure
Bnmr

## Slide 36
[local:expt:Stopped]/Experiment>cd Security/
[local:expt:Stopped]Security>ls -lr
Key name Type #Val Size Last Opn Mode Value
---------------------------------------------------------------------------
Security DIR
Allowed hosts DIR
host.sample.domain INT 1 4 >99d 0 RWD 0
host1.triumf.ca INT 1 4 >99d 0 RWD 0
host2.triumf.ca INT 1 4 >99d 0 RWD 0
host3vw INT 1 4 >99d 0 RWD 0
host4vw2 INT 1 4 >99d 0 RWD 0
Allowed programs DIR
mstat INT 1 4 >99d 0 RWD 0
Password STRING 1 32 >99d 0 RWD mojnNsGpGtzw4
Web Password STRING 1 32 >99d 0 RWD mnm6NtsnORgri
OdbEdit: /Experiment/Security (hidden)
Invoked by ODB> webpasswd
Created by ODB> passwd
Provides access control to declared tasks and/or hosts as well as general user access
to the experiment and R/W from the Web browser.
Comments:
By default public Read/Write access to the database.
“webpasswd” public Write protection
“passwd” public Read/Write protection.
ODB structure
DEMO/TWIST

## Slide 37
OdbEdit: /Logger/Elog dir & /Logger/History dir (hidden)
Provides dedicated path for the storage of the Elog files as well as the History files.
[local:twist:Stopped]/Logger>ls -lr
Key name Type #Val Size Last Opn Mode Value
---------------------------------------------------------------------------
Logger DIR
Data dir STRING 1 256 22s 0 RWD /data_onl/current
Message file STRING 1 256 22s 0 RWD midas.log
Auto restart BOOL 1 4 22s 0 RWD y
Write data BOOL 1 4 22s 0 RWD y
ODB Dump BOOL 1 4 22s 0 RWD y
ODB Dump File STRING 1 256 22s 0 RWD run%05d.odb
Tape message BOOL 1 4 22s 0 RWD y
Channels DIR
0 DIR
Settings DIR
Active BOOL 1 4 22s 0 RWD y
Type STRING 1 8 22s 0 RWD Disk
Filename STRING 1 256 22s 0 RWD run%05d.ybs
Format STRING 1 8 22s 0 RWD YBOS
ODB dump BOOL 1 4 22s 0 RWD n
Log messages DWORD 1 4 22s 0 RWD 0
Buffer STRING 1 32 22s 0 RWD SYSTEM
Event ID INT 1 4 22s 0 RWD -1
Trigger mask INT 1 4 22s 0 RWD -1
Event limit DWORD 1 4 22s 0 RWD 0
Byte limit DOUBLE 1 8 22s 0 RWD 2e+09
Tape capacity DOUBLE 1 8 22s 0 RWD 0
Subdir format STRING 1 32 22s 0 RWD
Current filenameSTRING 1 256 22s 0 RWD run13597.ybs
Statistics DIR
…
1 DIR
Settings DIR
Active BOOL 1 4 22s 0 RWD y
Type STRING 1 8 22s 0 RWD Disk
Filename STRING 1 256 22s 0 RWD srun%05d.ybs
Format STRING 1 8 22s 0 RWD YBOS
ODB dump BOOL 1 4 22s 0 RWD n
Log messages DWORD 1 4 22s 0 RWD 0
Buffer STRING 1 32 22s 0 RWD SYSTEM
Event ID INT 1 4 22s 0 RWD -1
Trigger mask INT 1 4 22s 0 RWD 32768
Event limit DWORD 1 4 22s 0 RWD 0
Byte limit DOUBLE 1 8 22s 0 RWD 2e+09
Tape capacity DOUBLE 1 8 22s 0 RWD 0
Subdir format STRING 1 32 22s 0 RWD current_split
Current filenameSTRING 1 256 22s 0 RWD current_split/srun13597.ybs
Statistics DIR
…
History dir STRING 1 256 22s 0 RWD /data_onl/elog_history
Elog Dir STRING 1 23 22s 0 RWD /data_onl/elog_history
ODB structure
TWIST

## Slide 38
Web Browser: /Alias (hidden)
[local:dragon:Stopped]/alias>ls –lr  HIT <Tab>
Myscalers&
FCup&
[local:dragon:Stopped]/alias>ls –lr  Hit <Ret>
Key name Type #Val Size Last Opn Mode Value
---------------------------------------------------------------------------
alias DIR
Sums DIR
Gammas_presented DOUBLE 1 8 13h 1 RWD 2.75257e+07
Gammas_acquired DOUBLE 1 8 13h 0 RWD 2.71811e+07
HI_presented DOUBLE 1 8 13h 0 RWD 6410
HI_acquired DOUBLE 1 8 13h 0 RWD 6073
Elastics_TSCA DOUBLE 1 8 13h 0 RWD 12690
Prescaled-TSCA DOUBLE 1 8 13h 0 RWD 1618
End-Det.-Triggers DOUBLE 1 8 13h 0 RWD 4793
Gamma-Sum-LED DOUBLE 1 8 13h 0 RWD 1.24667e+08
Pulsers DOUBLE 1 8 13h 0 RWD 4319
Beta-monitor DOUBLE 1 8 13h 0 RWD 0
Elastics-CFD DOUBLE 1 8 13h 0 RWD 1.69766e+08
Beta-monitor-singles DOUBLE 1 8 13h 0 RWD 938
FCup& STRING 1 64 5h 0 RWD
http://midmes01.triumf.ca:8081/HS/Beam?exp=dragon
Provides shortcut to ODB location. Will appear in the Web browser as hyperlink.
Comments:
/Alias/<shortcut> spawn new frame with the shortcut destination
/Alias/<shortcut&> replace current frame content with shortcut destination
ODB structure
Result
Dragon

## Slide 39
#
# determine equipment name from beamline
#
if($beamline =~ /bn[qm]r/i)
{
# BNMR experiments use equipment name of FIFO_ACQ
$eqp_name = "FIFO_ACQ";
}
else
{
# All MUSR experiments use equipment name of MUSR_TD_ACQ
$eqp_name = "MUSR_TD_ACQ";
}
$mdarc_path= "/Equipment/$eqp_name/mdarc/";
print FOUT "mdarc path: $mdarc_path\n";
# check whether run is in progress
($run_state,$transition) = get_run_state();
if($DEBUG) { print FOUT "After get_run_state, run_state=$run_state, trans=$transition\n"; }
if ($run_state != $STATE_STOPPED)
{ # Run is going
# return
if ($ppg_mode =~ /^2/i) # match 2 at beginning of string (e.g. 2a)
{
print FOUT "Run in progress. Use Toggle button to change run type \n";
($status)=odb_cmd ( "msg","$MINFO", "","$name", "WARNING - run is in progress.
Use toggle button to change run type" ) ;
unless ($status) { print FOUT "$name: Failure status after odb_cmd (msg)\n"; }
die " Run is in progress. Use Toggle button to change the run type\n";
}
else # Type 1
{
print FOUT "Run in progress.
Run type cannot be changed while run is in progress \n";
($status)=odb_cmd ( "msg","$MINFO", "","$name", "WARNING - Run type cannot be
changed while run is in progress " ) ;
unless ($status) { print FOUT "$name: Failure status after odb_cmd (msg)\n"; }
die " Run type cannot be changed while run is in progress\n";
}
[local:bnmr1:S]/>cd Script/
[local:bnmr1:S]/Script>ls -lr
Key name Type #Val Size Last Opn Mode Value
---------------------------------------------------------------------------
Script DIR
BNQR Hold DIR
cmd STRING 1 128 >99d 0 RWD /home/bnqr/online/mdarc/perl/hold.pl
include path STRING 1 64 >99d 0 RWD /home/bnqr/online/mdarc/perl
Name STRING 1 32 31s 0 RWD bnqr
hold BOOL 1 4 6h 0 RWD n
toggle BOOL 1 4 >99d 0 RWD n
beamline STRING 1 5 >99d 0 RWD bnqr
Continue DIR
cmd STRING 1 128 >99d 0 RWD /home/bnqr/online/mdarc/perl/continue.pl
include path STRING 1 64 >99d 0 RWD /home/bnqr/online/mdarc/perl
Name STRING 1 32 31s 0 RWD bnqr
hold BOOL 1 4 6h 0 RWD n
beamline STRING 1 5 >99d 0 RWD bnqr
Web Browser: /Script (hidden)
Provides Web browser shortcut for activation of script.
Will appear in the Web browser as hyperlink after any “alias” links.
Comments:
/Script/<Button name>/ Key type (dir). Will appear on the Midas status page.
  <command> Command string.
  <arg or link> Argument passed to the script.
  <arg or link> Argument passed to the script.
No limits on the number of argument passed to the script.
ODB structure
Result
Bnmr
Perl code

## Slide 40
Web Browser: /Custom (hidden)
Provides custom Web page with Midas specific HTML tags.
Comments:
Standard HTML syntax.
Result
[local:dragon:Stopped]/>cd Custom/
[local:dragon:Stopped]/Custom>ls RunSummary&
RunSummary&
…
<font size=5 face="Arial,Helvetica"><b><center>Current DRAGON Status</center></b></font>
<p> <center>
<table align=center width=90%><tr><td>
<form method="GET" action="http://isdaq04:8081/CS/RunSummary&">
<input type=hidden name=exp value="dragon">
<center>
<input type=submit name=cmd value=Status>
<input type=submit name=cmd value=Start>
<input type=submit name=cmd value=Stop>
<input type=submit name=cmd value=ODB>
<input type=submit name=cmd value=History>
<input type=submit name=cmd value=ELog>
</center> <p> <center>
<table border=0>
<tr><td>Last Run: </td> <td><odb src="/Runinfo/Run number"></td></tr>
<tr><td>Start Time: </td> <td><odb src="/Runinfo/Start time"></td></tr>
<tr><td>Stop Time: </td> <td><odb src="/Runinfo/Stop time"></td></tr>
</table>
<p> <table>
<tr><td>Run Details: </td><td><odb src="/Experiment/Run Parameters/Comment"></td></tr>
</table> </center>
<p> <center>
<table border=0 bgcolor=#000000 cellpadding=5 width=675>
<tr>
<td align=center colspan=2><b>
<font color=#FFFFFF face="Arial,Helvetica">Gas Target</font></b></td> </tr> <tr>
<td bgcolor=#ffffff width=150><font size="-1"><b>Cell pressure: </b></font></td>
<td bgcolor=#ffffff width=525><font size="-1">
<odb src="/Equipment/NewEpics/Variables/EpicsVars[0]"> torr</font></td>
</tr>
…
“Run Summary&
html content
[local:dragon:Stopped]/>cd Custom/
[local:dragon:Stopped]/Custom>ls RunSummary&
RunSummary&
ODB structure
Result
Dragon

## Slide 41
Web Browser: /Custom example